# Annex No 1

ENVIRONMENTAL ACCESSIBILITY ASSESSMENT QUESTIONNAIRE

Institution _____________________________________________

Address_________________________________________________

1.  External environment

1.1. Car parking

| No | To check: | Rating (0 – not at all, 1- partially met, 2- fully met) | Does not apply If it doesn’t apply mark with an X |
| --- | --- | --- | --- |
| 1 | Is there at least one parking place for People with Disability (PwD)? |  |  |
| 2 | Is the parking place for PwD large enough (min. - 3.9 m wide and 5 m long)? |  |  |
| 3 | Is the parking place for PwD marked with a special sign? |  |  |
|  | TOTAL |  |  |
| ! The average rating (points marked with “X” are not taken into account in calculating the average rating) |

1.2. Access from the street/parking place to the main entrance of the building and pavement

| No | To check: | Rating (0 – not at all, 1- partially met, 2- fully met) | Does not apply If it doesn’t apply mark with an X |
| --- | --- | --- | --- |
| 4 | Is public building entrance, front area of elevators, and other accesses areas, as well as other rooms for visitors designed without any thresholds? Ramps are necessary if there is difference in height levels between rooms or the building and the pavement. |  |  |
| 5 | Is surface for accessing the building flat and solid (asphalt or other) for use by people with mobility impairments, in wheelchairs or with buggies? |  |  |
| 6 | Is the height proportion of the external ramp not higher than 1:12 (8%)? |  |  |
| 7 | Is the width of the movement road at-least 1.2 m? |  |  |
| 8 | Are access roads, which are longer than 12 m, at least 1.8 m wide or do they have 1.8 m wide area for stopping or exchange after every 12 m? |  |  |
| 9 | Is access path well-lit? |  |  |
| 10 | Does not the access path have any obstacles in the way and any confusing signs? |  |  |
| 11 | Are all kinds of posts (traffic light, road sign, advertising and lighting posts) marked with contrasting colour or with tape in the height of 160 cm, 140cm and 35 cm? |  |  |
|  | TOTAL |  |  |

! The average rating (points marked with “X” are not taken into account in calculating the average rating)

1.3. Stairs and ramps (outdoors and indoors)

| No | To check: | Rating (0 – not at all, 1- partially met, 2- fully met) | Does not apply If it doesn’t apply mark with an X |
| --- | --- | --- | --- |
| 12 | Is there floor number in Braille on handrails by the first and the last step of stairs? |  |  |
| 13 | Are there any visual warnings before the stairs detectable, both: at the top and bottom? (a 10 cm wide warning should be placed along the entire stair width) |  |  |
| 14 | Is the edge of each step in its entire width marked so that it contrasts with the rest of the stairs? |  |  |
| 15 | Is the width of the wheelchair ramp at least 1.2 m? |  |  |
| 16 | Are stairs and ramps equipped with railing with handles in contrasting colours on both sides? Do the railings have two levels at the height of 0.7 m and 0.9 m? The railings should be 0.3 m longer than stairs or ramp on both ends. The railing should accurately follow stair contours, providing direction, orientation and safety. |  |  |
| 17 | Does the ramp that is longer than 6 m has a minimum of one horizontal rest field with the area of 1.5 m x 1.5 m after every 3 m? |  |  |
| 18 | Does the gradation proportion outdoors have the minimum of 1:12 (8%) by public buildings and 1:20 (5%) by residential buildings? |  |  |
| 19 | Is the ascent steepness indoors less than 1:12 (8%) in hotel and sanatorium rooms and 1:20 (5%) in residential buildings? |  |  |
| 20 | Are all areas with level change (end and beginning of stairs, ascents) marked with 5 cm wide bright and contrasting colour warnings (in yellow or in dark on a light background) in the entire width of the stairs or ascent? |  |  |
|  | TOTAL |  |  |

! The average rating (points marked with “X” are not taken into account in calculating the average rating)

1.5. Signs and indications (outdoors and indoors)

| No | To check: | Rating (0 – not at all, 1- partially met, 2- fully met) | Does not apply If it doesn’t apply mark with an X |
| --- | --- | --- | --- |
| 21 | Are there any signs and indications directing towards stairs, evacuation exits etc.? |  |  |
| 22 | Is the height of letters in indications at least 5 cm? Are indications placed in the height of 1,4-1,6m and can be read from 2 m distance? |  |  |
| 23 | Are images/symbols/icons used as an alternative to text on the signs? |  |  |
| 24 | Are the indications well illuminated? |  |  |
| 25 | Is the change of queue number not only displayed but also announced by sound in establishments where the queues are being regulated mechanically? |  |  |
| 26 | Are indications placed so that they are easy to access and read? |  |  |
| 27 | Do indications sufficiently contrast with the surrounding environment? |  |  |
|  | TOTAL: |  |  |

! The average rating (points marked with “X” are not taken into account in calculating the average rating).

2. Interior

2.1. Entrance, publicly accessible rooms, residential houses

| No | To check: | Rating (0 – not at all, 1- partially met, 2- fully met) | Does not apply If it doesn’t apply mark with an X |
| --- | --- | --- | --- |
| 28 | Does the door open and close automatically? |  |  |
| 29 | Are the door bells, card readers, door handles adjusted in the height of 0.9-1.1 m from ground? Are the window handles in reachable height? |  |  |
| 30 | Is the access to entering and moving around the building fit for people with mobility impairments, people in wheelchairs and with prams? And are the necessary assisting devices/equipment available in particular rooms (e.g. hotel rooms, toilets)? |  |  |
| 31 | Do public buildings higher than one floor have at least 1 elevator or moving staircase for public use or another solution suitable for people with special needs? |  |  |
| 32 | Is there at least one toilet room for wheelchair users on each floor? |  |  |
| 33 | Are toilet rooms for wheelchair users accessible: 1) in public buildings minimum cabin width 1,6m, minimum length 1,8m; 2) in residential houses minimum cabin width 1,4m or 1,6m (if there is a sink), minimum length 2,2m? |  |  |
| 34 | Is customer reception/service area organized in accessible place, easily to be found? |  |  |
| 35 | Is it possible for people with sight or hearing impairments to receive necessary audio or visual information? |  |  |
| 36 | Are premises equipped with easily perceptible (contrasting and well illuminated) signs and indications? |  |  |
| 37 | Are the shower rooms for use of people in wheelchairs with the minimum width and length of 1,7m? |  |  |
|  | TOTAL: |  |  |

! The average rating (points marked with “X” are not taken into account in calculating the average rating).

2.2. Corridors

| No | To check: | Rating (0 – not at all, 1- partially met, 2- fully met) | Does not apply If it doesn’t apply mark with an X |
| --- | --- | --- | --- |
| 38 | Aren`t there any steps on the way to rooms? |  |  |
| 39 | Is floor surface mat? |  |  |
| 40 | Aren`t there any carpets/rugs on the floor? |  |  |
| 41 | Are corridors wide enough for wheelchair users? Free width at least 1.5 m in public buildings and at least 1.8 m in residential buildings? |  |  |
| 42 | Is equipment placed out of the way in the main movement routes? |  |  |
| 43 | Is there enough space for the wheelchair-user to turn around (min. 1.5 m x 1.5 m)? |  |  |
| 44 | Isn`t the equipment placed below knee hight in hallways and common use areas and isn`t it endangering safe mobility of a blind person? |  |  |
| 45 | Do the walls, floors and doors in evacuation paths contrast with the surroundings in order to facilitate orienteering in the building? |  |  |
| 46 | Is the system of indications consecutive for finding the right room? |  |  |
| 47 | Is there sufficient general lighting? |  |  |
| 48 | Aren`t there any direct and bright light sources in hallways? |  |  |
| 49 | Do windows have sun covers? |  |  |
|  | TOTAL: |  |  |

! The average rating (points marked with “X” are not taken into account in calculating the average rating).

2.3. Doors

| No | To check: | Rating (0 – not at all, 1- partially met, 2- fully met) | Does not apply If it doesn’t apply mark with an X |
| --- | --- | --- | --- |
| 50 | Do the doors stay open while the visitor is in the door operation area? |  |  |
| 51 | Is the door`s free width at least 90 cm in public buildings and at least 120 cm (external door) in residential buildings? |  |  |
| 52 | Is the opener of automatic door or card reader placed in the hight of 0.9 -1.1m above the ground level? |  |  |
| 53 | Does the opener of automatic door or card reader contrast with the background and the surrounding environment? |  |  |
| 54 | Is the contrasting colouring on the glass doors and walls consistent and is the colouring`s top edge placed in the height of 160 cm, 140 cm and 35 cm from the ground level? The contrasting marking must be 10 cm wide. |  |  |
| 55 | Do doors and door frames contrast with surrounding walls? |  |  |
|  | TOTAL: |  |  |

! The average rating (points marked with “X” are not taken into account in calculating the average rating).

2.4. Elevators

| No | To check: | Rating (0 – not at all, 1- partially met, 2- fully met) | Does not apply If it doesn’t apply mark with an X |
| --- | --- | --- | --- |
| 56 | Is there a built-in warning field (different cover material) on the floor before the elevator? |  |  |
| 57 | Is every elevator cab at least 1.1 m x 1.4 m? |  |  |
| 58 | Do elevator doors contrast with the walls? |  |  |
| 59 | Is elevator floor not slippery? |  |  |
| 60 | Is the required information also available in Braille? |  |  |
| 61 | Are all panels and buttons inside and outside the elevator placed in the height of 0.9-1.1 m above the ground level? |  |  |
| 62 | Are panels and buttons inside and by the elevator marked with large and clear numbers? |  |  |
| 63 | Are the railings in the height of 0.9m? |  |  |
| 64 | Is there sufficient lighting in the elevator? |  |  |
|  | TOTAL: |  |  |

! The average rating (points marked with “X” are not taken into account in calculating the average rating).

Institution’s total average rating:________________________points.

(Total average rating = average of all rated issues block amount divided by the number of units measured, max 10 points)